## Slide 1
TankGuard
Self-powered IoT water-tank monitoring, pump control and automated sludge cleaning
Dr. Vishnu Vasudev

## Slide 2
Key Points:
- Three local units, one LAN: M1 monitor, H1 home display + pump control, C1 cleaning arm.
- Edge-computed TankScore from five submerged probes; no cloud, no account.
- Dashboard served by the tank unit itself, over its own Wi-Fi.
- Cleaning arm covers 90% of the tank floor per cycle and parks at both ends.
- TRL 6+ in 12 months with three field installations.
Guidelines

## Slide 3
Water storage tanks degrade silently: disinfectant residual dissipates within 24-48 hours, particles settle into a sludge layer, biofilm forms on the walls, and algae bloom in warm water. By the time the water smells or looks wrong it is unsafe, and the only remedy is a full drain and manual scrub that wastes the whole stored volume.
Problem Statement

## Slide 4
M1 sits on the lid: five submerged probes through an ADS1115, an edge TankScore, and a web dashboard served from its own flash. H1 sits by the pump: a 1.8" display, automatic level control through an isolated relay and contactor, and a manual override. C1 is a two-link 20 cm + 20 cm arm that sweeps three concentric rings with a ring brush and draws the loosened sludge out through the centre of the head.
Solution

## Slide 5
Unique points:
1. Closed-loop care: sense, score, act, verify - with the verification shown, not claimed.
2. Local-only architecture: no cloud path, no account, works when the internet does not.
3. Selective cleaning: 90% floor coverage per cycle without draining the tank.
4. Honest instrumentation: the dashboard states its data source and the arm's 2 cm wall ring.
USP / Differentiator

## Slide 6
Quantified impact:
- No full drain: cleaning removes the sludge layer, not the stored volume.
- Pump protection: level-based automatic control with a safe manual override.
- Early warning: a score trend catches degradation before smell or taste.
- Off-grid: solar + battery keeps the monitor alive for weeks without sun.
Impact

## Slide 7
Methodology:
M1 (T0+2): probes, TankScore, dashboard served from flash.
H1 + dashboard (T0+4): TFT, pump control, session log, device table.
C1 (T0+8): 2R arm, planner, controller, three-ring cycle.
Field (T0+12): three installations, 90 days, TRL 6+ evidence.
Project Plan / Methodology

## Slide 8
 | Milestone Details | Time Period Required from To (To Being Project Start Date)
1 | Requirements and monitor prototype | T0 + 2 months
2 | Home unit and dashboard | T0 + 4 months
3 | Cleaning arm | T0 + 8 months
4 | Field validation | T0 + 12 months
Milestones:
1 Requirements and monitor prototype - T0 + 2 months
2 Home unit and dashboard - T0 + 4 months
3 Cleaning arm - T0 + 8 months
4 Field validation - T0 + 12 months

## Slide 9
Market: domestic and institutional water storage tanks - homes, apartment buildings, schools, hospitals and small industry. The buyer is the same person who pays the plumber today; the value is water saved, pump life and a measurable answer to "is my water safe?".
Market Size

## Slide 10
Resources and budget (indicative, excl. GST):
M1 monitor: INR 6,500
H1 home unit: INR 1,800
C1 cleaning arm: INR 7,300
Equipment total: INR 15,600; with contingency, overhead and faculty fee: INR 23,587.
Sr. No | Item | T0 | T0+6 | Total (Add more columns if required)
Resources & Budget

## Slide 11
Funding so far: not yet secured. Nuke Labs is committed as the industry partner for build facilities, field access and TRL 6+ validation.
Funding So Far

## Slide 12
Team:
Principal Investigator: Dr. Vishnu Vasudev, Department of Electronics and Communication Engineering.
Industry partner: Nuke Labs - hardware build, field installations, commercialisation.
Team

## Slide 13
TankGuard turns tank maintenance from calendar guesswork into measured care: sensing at the edge, deciding locally, cleaning selectively, and showing its own evidence.